## Slide 1: Speaker Recognition System EEC 201
Team: El Tirado

## Slide 2: Outline
Introduction
Motivation
Methodology
  Training / testing phase
  DSP aspects
  Pattern recognition aspects
Evaluation and Results
  Datasets
  Training/Testing accuracies
  Introduction of new users to the system
  Robustness of the system
  Ablation study
Discussion
Conclusion

## Slide 3: Introduction
Speaker recognition is the task of identifying the narrator of a voice segment using characteristics of voices.
Comes with a pre-stored database of users and their characteristics
Once deployed, any voice segment is compared with the database and try to correctly identify the user
? ? ? ?

## Slide 4: Motivation
Speaker recognition is a popular, but challenging task
Like our fingerprint we can use voice for authentication purposes.
New approaches uses machine learning and deep neural networks ( CNNs ) with copious amount of data.
Yet proper DSP tools combined with simple pattern recognition tools can produce very efficient and accurate recognition system.

## Slide 5: Methodology > System Overview
Designing a speaker recognition system follows two essential steps
  Training phase
  Testing phase

## Slide 6: Methodology > System Overview > Training Phase
User1
User2
User-N
User3
Codebook generation
Feature extraction
Input signal
Training
Codebook1
Codebook2
Codebook3
Codebook-N
Click to add text

## Slide 7: Methodology > System Overview > Testing Phase
Feature extraction
Input signal
Testing
User ID?
User1
User2
User-N
User3
Codebook1
Codebook2
Codebook3
Codebook-N
Min distance

## Slide 8: Methodology > DSP > Feature Extraction ( MFCC )
Click to add text
Frame Blocking
Windowing
Mel-frequency Wrapping
FFT and Power Spectrum
Cepstrum
Frame
Spectrum
Mel
spectrum
Mel
cepstrum
Pre-Emphasis
Coefficient Normalization
Feature Matching

## Slide 9: Methodology > DSP > Pre-Emphasis
Amplifies the high frequencies of the input signal.
provides
  a good signal-to-noise ratio
  stabilizes the numerical calculations of the Fourier Transform
  and balances the frequency spectrum

## Slide 10: Methodology > DSP > Frame Blocking and Windowing
In many applications related to voice, processing after the arrival of the complete signal carries no importance.
Instead of processing the complete signal at once we split the signal into overlapping frames.
For a given short time period, frequencies of a signal have a stationary property.
We can accurately approximate the Fourier representation of the signal.
We represent one frame by (𝑁) 256 samples and the number of overlapping samples to (𝑀) 100.
We apply a window on top of each frame.
Windowing helps to mitigate any spectral leakage.
Hamming window -

## Slide 11: Methodology > DSP > FFT and PSD
Take Fourier Transform (FT) of each frame
We can use the Fast Fourier Transform (FFT)
FT provides the frequency domain representation but power spectral density (PSD) as it provides better and deterministic characteristics than FT.

## Slide 12: Methodology > DSP > Mel Frequency Wrapping and Cepstrum
The mechanism of human ear can be model using Mel model
Once we know about the frequencies that contains the most power, convert it to the Mel domain using filter banks.
Apply Discrete Cosine Transform ( DCT) on the results and obtain cepstrum ( a list of coefficients. )
The crucial information is embedded in 2 – 13 th coefficients
Extract above coefficients and these will be robust representation of the voice segments and we call it the feature vector.

## Slide 13: Feature Matching > LBG Algorithm
Notes: After extracting MFCCs from the input voice sample, we should then design a way to recognize the speaker based on these voice features.
This process can be accomplished by the well-know LBG algorithm
The overall workflow of the LBG algorithm is presented in the following figure
To begin with, the algorithm will initialize a single-vector codebook representing the centroid of all training vectors. Then, it will double the size of the codebook by splitting each current codebook $cb_{n}$ according to the equation in the left
In this equation, cb_{n} represent the current codebook and epsilon is a splitting parameter and be set to 0.01 in this project.
Also, small m here is the number of current codebook
After spliting the codebook, we will update the centroid of codebook to create a new set of codebooks.
We can see that in each iteration, the size of the codebook will be doubled. The algorithm would repeat this process until the number of codebooks meet our requirement.
That is, when small m is less than capital M, the iteration will be terminated
Here M is set to be 8 in this project.

## Slide 14: Feature Matching > LBG Algorithm
Notes: We now show the visualization of LBG algorithm's executing process
On the right figure
Black dot represent the extracted features
We only select two dimension of the feature as an example
So the algorithm will first initialize with a single codebook
Here you can see from the figure that green dot is the current codebook

## Slide 15: Feature Matching > LBG Algorithm
Notes: Then, the algorithm will double the current code by splitting
As the figure shows
there are two green dots now

## Slide 16: Feature Matching > LBG Algorithm
Notes: Next the algorithm will update the centroid of each codebook
As the figure shows
The green dots are now moved to the center of each cluster

## Slide 17: Feature Matching > LBG Algorithm
Notes: Next the algorithm will check if current size of codebook has meet the requirement
Because we only have two codebook now and is less than eight codebook
The iteration will continue

## Slide 18: Feature Matching > LBG Algorithm
Notes: In the next iteration, we again double the codebook by splitting

## Slide 19: Feature Matching > LBG Algorithm
Notes: And then update the centroid of each codebook

## Slide 20: Feature Matching > LBG Algorithm
Notes: Check the condition and then proceed to another iteration

## Slide 21: Feature Matching > LBG Algorithm
Notes: This is the final iteration
We can see that we has eight green dots after splitting

## Slide 22: Feature Matching > LBG Algorithm
Notes: Update the centroid of these eight codebook

## Slide 23: Feature Matching > LBG Algorithm
Notes: Check the termination condition
And the algorithm will stop
So these eight green dots are the output of the algorithm that represent the codebook we use to recognize the speakers

## Slide 24: Evaluation on Training Data
Notes: Finally,
We evaluate the performance of our speaker recognition system
Each row illustrates the distance from the training sample to each training user.
The distance value is measured by L_2 norm
And the prediction is based on selecting the minimum distance value of each possible speaker's codebook
We can concentrate on the diagonal elements, which means the distance value of ground truth user to the prediction user
We can see that our system correctly recognize all of the speaker in the training set

## Slide 25: Evaluation on Testing Data
Notes: Following the same set up
We now evaluate our system with the testing data
We can see that our system can still have 100% accuracy on the testing data

## Slide 26: Evaluation on Introducing New Users
Notes: Next, we add two voice sample from two of our teammate
They are labeled as s12 and s13
We can see that even with the new users
Our system can still remain 100% accuracy
However, since the number of new users is limited in our experiment,
we can only conclude that the performance of our system can preserve robustness to new users when the number of total users remains low

## Slide 27: Evaluation on Different Phrases
Distance value in (s13, s13):
  Yes: 0.028
  ごめんなさい: 0.0362
  為什麼: 0.0289
Notes: We have also test the performance when the new user s13 saying different phrase
This table shows the prediction result when s13 saying Yes in English instead of zero
We can see that even though the user s13 can be recognized,
The performance of other users are being affected
For exaple, we mispredict ground truth user s5 to s7
And we are on the edge of misprediction for user s1 and s7
Other than english, we also test the phrase in japaness and chinese
Their result is similar
We can still detect the user s13 with distance of 0.0362 and 0.0289
But the performance of other users are being affected

## Slide 28: Ablation Study
Notes: Finally, we perform an ablation study on our system by removing the pre-emphasis function block.
As we can see from the table,
the model miss classifies user 1 as user 4.
Furthermore, if we move along the elements in this table 5 and compare with the corresponding entries in the previous table with pre emphasis
the distance gaps in the entries of table 5 are small.
That is, we can strengthen the confident levels of the predictions using the pre-emphasis block.

## Slide 29: Conclusion
In this project, we explored the concurrent use of Digital Signal Processing and pattern recognition in identifying the user of a given voice sample.
Among an ample number of methods, we utilize the use of a simple and very efficient approach of vector quantization and show ideal performance in given datasets.
We see such a method can achieve expected accuracy with no leverage on computation complexity, memory usage, and execution time.
Notes: In summary, our conclusion of this project is that
We explored the concurrent use of Digital Signal Processing and pattern recognition in identifying the user of a given voice sample.
We also illustrate that our system can perform accurate speaker recognition with minimal set of training data
However, in order to make our system more accurate and expand our system to a more challeging setting
We need more related training data
and the performance will be better when considering state of the art machine learning technology

## Slide 30: Reference
[1] Haytham M. Fayek. 2016. Speech Processing for Machine Learning: Filter banks, Mel-Frequency Cepstral Coefficients (MFCCs) and What’s In-Between. https://haythamfayek.com/2016/04/21/speech-processing-for-machine-learning.html
[2] Y. Linde, A. Buzo, and R. Gray. 1980. An Algorithm for Vector Quantizer Design. IEEE Transactions on Communications 28, 1 (1980), 84–95. https://doi.org/10.1109/ TCOM.1980.1094577
[3] Lindasalwa Muda, Mumtaj Begam, and Irraivan Elamvazuthi. 2010. Voice Recogni- tion Algorithms using Mel Frequency Cepstral Coefficient (MFCC) and Dynamic Time Warping (DTW) Techniques. ArXiv abs/1003.4083 (2010).

## Slide 31: Evaluation on the Filtered Testing Data